|  | PM B Checklist | In cab |
| --- | --- | --- |
|  |  |  | Report any cleanliness issues to supervisor |
|  | Check mark or “OK” indicates pass |  |  |
|  | N indicates needed repair |  | Windshield |
|  | (repairs must be listed separately on repair order) |  | Mirror condition and mounting |
|  | N indicates repair completed |  | Gauges |
|  |  | Interaxle differential control |
| Unit number: Plate number: Assigned driver: Date: Mileage: Start time: End time: Technician: |  | Air suspension control |
|  |  | Shifter play |
|  |  | Pedal action |
|  |  | Clutch freeplay |
|  |  | Steering freeplay/lash |
|  |  | Light indicators (L, R, HB) |
|  |  | Dash lights |
|  |  | Dome lights |
|  |  |  | Wiper controls |
| Before starting PM |  | Brake controls |
|  |  | Seat Adjustment |
|  | Pull any outstanding work orders or driver inspection reports and review Check recall, technical bulletin, and outstanding repair boards |  | Air brake check Leaks Air warning Button pop-out |
|  | Check mileage since last PM A and B | Electrical |
|  | Check mos. and mileage since last PM C |  |  |
|  | Check for outstanding PM D |  | Check battery/terminal condition |
|  | Check for new permits or plates |  | Load check batteries |
|  | Get necessary parts |  | Test 120 plug in |
|  | Fresh damage Y/N |  | Check system with ammeter/voltmeter |
|  | Place LOTO sign in/on vehicle |  | Check ammeter/voltmeter on dash |
|  |  |  | Download ECM/EDR |
|  | Report any cleanliness issues or fresh damage to supervisor immediately. |  | Check for fault codes |
|  |  |  | Report any issues to supervisor |
| All lights |  |  |
|  |  | Under hood |
|  | Headlights: Low ___ High ___ |  |  |
|  | ID Marker lights |  | General condition and leaks |
|  | Clearance lights |  | Electrical connections |
|  | Midline signal and marker (if equipped) |  | Air connections and leaks |
|  | Worklight(s) |  | Oil level before oil and filter change |
|  | Fog/road lights (if equipped) |  | Oil level after change: Added |
|  | All signals: Left __ Right __ Hazard __ |  | Coolant level: Added |
|  | Brake lights |  | Coolant strength |

|  | Coolant filter: Last changed |  | Slack adjusters: Lubricated Y/N |
| --- | --- | --- | --- |
|  | Replaced Y/N |  | S-Cams/S-cam bearings: Lubricated Y/N |
|  | Power steering fluid: Added |  | Brake drums |
|  | Transmission fluid: Added |  | Brake shoes/pads |
|  | Belt condition and tension: Adjusted Y/N |  | Brake linings: Thickness L __ R __ |
|  | Air compressor |  | Hub oil leakage |
|  | Fuel pump |  | Hub oil level: Added L __ R __ |
|  | Fan clutch engagement and fan condition Air filter: Last changed |  | Lower steering arms and associated ball joints: Lubricated Y/N |
|  | Replaced Y/N |  | Tie rod |
|  | Fuel filter: Last changed |  | Kingpins: Lubricated Y/N |
|  | Replaced Y/N |  | Alignment checked Y/N |
|  | Fuel/water separator |  | Tire tread depth: L __/32 R __/32 |
|  | Air dryer cartridge/function: |  | Tire inflation: Before filling L __ R __ |
|  | Last changed ____ |  | After filling L __ R __ |
|  | Replaced Y/N |  | Tire condition |
|  | Radiator screen |  | Rims |
|  | Turbo charger |  | Lugs: Torque check Y/N |
|  | Exhaust leaks |  | Tightened Y/N |
| Steering assembly | Cab/body/frame |
|  | Steering column: Lubricated Y/N |  | Frame, crossmembers, body mounts |
|  | Steering gear box |  | Doors, door seals, and windows |
|  | Pitman arm/ball joint: Lubricated Y/N |  | Mirrors |
|  | Drag link/ball joint: Lubricated Y/N |  | Emergency equipment |
|  | Upper steering arm/joint: Lubricated Y/N |  | Triangles |
|  |  |  | Extinguisher |
| Steer axle (both sides) |  | Spare fuses |
|  |  |  | Fuel tank |
|  | Spring hangers/shackles: Tightened Y/N |  | Fuel lines |
|  | Lubricated Y/N |  | Wipers |
|  | U-Bolts: Tightened Y/N |  | Windshield |
|  | Springs |  | Mirror mounts |
|  | Shock absorbers |  |  |
|  | Brake chamber air lines |  |  |
|  | Brake chambers |  |  |
|  | Brake push rods and clevis/clevis pins |  |  |
|  | Brake adjustment: Free-play before adjustment L R |  |
|  | If adjustment was necessary, reason was determined |  |  |

| Drive wheel assembly |  | Tire condition |
| --- | --- | --- |
|  |  |  | Rims |
|  | Drive shaft: Lubricated Y/N |  | Lugs: Torque check Y/N |
|  | Interaxle differential |  | Tightened Y/N |
|  | Front differential: Added |  |  |
|  | Rear differential: Added Spring/arm hangers: Tightened Y/N | Upon completion |
|  | Lubricated Y/N |  |  |
|  | U-Bolts: Tightened Y/N |  | QC by supervisor |
|  | Springs/arms Air bags |  | Update recall, technical bulletin, repair, and PM board |
|  | Shock absorbers |  | Place new sticker on door/windshield/seat |
|  | Brake chamber air lines |  | Report vehicle as available |
|  | Brake chambers |  | Sign off on DVIR (if driver submitted one) |
|  | Brake push rods and clevis/clevis pins |  | Place DVIR in door pouch for driver |
|  | Brake adjustment: Free-play before |  | Complete work order(s) for PM and Repairs |
|  | adjustment LF___ LR ___ RF___ RR |  | Attach PM checklist to work order |
|  | If adjustment was necessary, reason was determined |  | Turn in all paperwork |
|  | Slack adjusters: Lubricated Y/N S-Cams/S-cam bearings: Lubricated Y/N |  | Report any non-driver reported defects discovered during PM to supervisor |
|  | Brake drums |  |  |
|  | Brake shoes/pads |  |  |
|  | Brake linings: Thickness LF___ LR ___ |  |  |
|  | RF___ RR |  |  |
|  | Hub leakage |  |  |
|  | Tire tread depth: | LFI __/32 | LFO __/32 |  |  |
|  |  | LRI __/32 | LRO __/32 |  |  |
|  |  | RFI __/32 | RFO __/32 |  |  |
|  |  | RRI __/32 | RRO __/32 |  |  |
|  | Tire inflation: |  |  |
|  | Before filling | LFI | LFO |  |  |
|  |  | LRI | LRO |  |  |
|  |  | RFI | RFO |  |  |
|  |  | RRI | RRO |  |  |
|  | After filling | LFI | LFO |  |  |
|  |  | LRI | LRO |  |  |
|  |  | RFI | RFO |  |  |
|  |  | RRI | RRO |  |  |